## Slide 1: Design of Digital Circuits Lecture 6: Sequential Logic Design
Prof. Onur Mutlu
ETH Zurich
Spring 2019
8 March 2019

## Slide 2: We Are Almost Done with This
Building blocks of modern computers
  Transistors
  Logic gates
Boolean algebra
Combinational circuits
How to use Boolean algebra to represent combinational circuits
Minimizing logic circuits

## Slide 3: Agenda for Today and Next Week
Today
  Wrap up Combinational Logic and Circuit Minimization
  Start (and finish) Sequential Logic
Next week
  Hardware Description Languages and Verilog
    Combinational Logic
    Sequential Logic
  Timing and Verification

## Slide 4: Extra Assignment 1: Lecture Video
Why study computer architecture?
Why is it important?
Future Computing Architectures
Required Assignment
  Watch my inaugural lecture at ETH and understand it
  https://www.youtube.com/watch?v=kgiZlSOcGFM
Optional Assignment – for 1% extra credit
  Write a 1-page summary of the lecture
    What are your key takeaways?
    What did you learn?
    What did you like or dislike?
    Upload PDF file to Moodle – Deadline: Friday, March 15.

## Slide 5: Extra Assignment 2: Moore’s Law (I)
Paper review
G.E. Moore. "Cramming more components onto integrated circuits," Electronics magazine, 1965
Optional Assignment – for 1% extra credit
  Write a 1-page review
  Upload PDF file to Moodle – Deadline: Friday, March 22
I strongly recommend that you follow my guidelines for (paper) review (see next slide)

## Slide 6: Extra Assignment 2: Moore’s Law (II)
Guidelines on how to review papers critically
  Guideline slides: pdf ppt
  Video: https://www.youtube.com/watch?v=tOL6FANAJ8c
  Example reviews on “Main Memory Scaling: Challenges and Solution Directions” (link to the paper)
    Review 1
    Review 2
  Example review on “Staged memory scheduling: Achieving high performance and scalability in heterogeneous systems” (link to the paper)
    Review 1

## Slide 7: Assignment: Required Readings
Combinational Logic
  P&P Chapter 3 until 3.3 + H&H Chapter 2
Sequential Logic
  P&P Chapter 3.4 until end + H&H Chapter 3 in full
Hardware Description Languages and Verilog
  H&H Chapter 4 in full
Timing and Verification
  H&H Chapters 2.9 and 3.5 + (start Chapter 5)
By the end of next week, make sure you are done with
  P&P Chapters 1-3 + H&H Chapters 1-4

## Slide 8: Wrap-Up Combinational Logic Circuits and Design

## Slide 9: Logic Simplification: Karnaugh Maps (K-Maps)

## Slide 10: Recall: Logic Minimization Using K-Maps
Very simple guideline:
  Circle all the rectangular blocks of 1’s in the map, using the fewest possible number of circles
    Each circle should be as large as possible
  Read off the implicants that were circled
More formally:
  A Boolean equation is minimized when it is written as a sum of the fewest number of prime implicants
  Each circle on the K-map represents an implicant
  The largest possible circles are prime implicants

## Slide 11: Recall: K-map Rules
What can be legally combined (circled) in the K-map?
  Rectangular groups of size 2k for any integer k
  Each cell has the same value (1, for now)
  All values must be adjacent
    Wrap-around edge is okay
How does a group become a term in an expression?
  Determine which literals are constant, and which vary across group
  Eliminate varying literals, then AND the constant literals
    constant 1 ➙ use , constant 0 ➙ use
What is a good solution?
  Biggest groupings ➙ eliminate more variables (literals) in each term
  Fewest groupings ➙ fewer terms (gates) all together
  OR together all AND terms you create from individual groups

## Slide 12: Recall: K-map Example: Two-bit Comparator
Design Approach:
Write a 4-Variable K-map
for each of the 3
output functions
A | B | C | D | F1 | F2 | F3
0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0
 | A |  | 
 |  | F1 | AB = CD
 | B |  | 
 |  | F2 | AB < CD
 | C |  | 
 |  | F3 | AB > CD
 | D |  | 

## Slide 13: Recall: K-map Example: Two-bit Comparator (2)
A | B | C | D | F1 | F2 | F3
0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0
 |  | 00 | 01 | 11 | 10
00 |  | 1 |  |  | 
01 |  |  | 1 |  | 
11 |  |  |  | 1 | 
10 |  |  |  |  | 1
K-map for F1
F1 =
A'B'C'D' + A'BC'D + ABCD + AB'CD'

## Slide 14: Recall: K-map Example: Two-bit Comparator (3)
A | B | C | D | F1 | F2 | F3
0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0
 |  | 00 | 01 | 11 | 10
00 |  |  | 1 | 1 | 1
01 |  |  |  | 1 | 1
11 |  |  |  |  | 
10 |  |  |  | 1 | 
K-map for F2
F2 =
A'C + A'B'D + B'CD
F3 =
? (Exercise for you)

## Slide 15: K-maps with “Don’t Care”
Don’t Care really means I don’t care what my circuit outputs if this appears as input
  You have an engineering choice to use DON’T CARE patterns intelligently as 1 or 0 to better simplify the circuit
I can pick 00, 01, 10, 11
independently of below
I can pick 00, 01, 10, 11
independently of above
A | B | C | D | F | G
• • • |  |  |  |  | 
0 | 1 | 1 | 0 | X | X
0 | 1 | 1 | 1 |  | 
1 | 0 | 0 | 0 | X | X
1 | 0 | 0 | 1 |  | 
• • • |  |  |  |  | 

## Slide 16: Example: BCD Increment Function
A | B | C | D | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | X | X | X | X
1 | 0 | 1 | 1 | X | X | X | X
1 | 1 | 0 | 0 | X | X | X | X
1 | 1 | 0 | 1 | X | X | X | X
1 | 1 | 1 | 0 | X | X | X | X
1 | 1 | 1 | 1 | X | X | X | X
BCD (Binary Coded Decimal) digits
  Encode decimal digits 0 - 9 with bit patterns 00002 — 10012
  When incremented, the decimal sequence is 0, 1, …, 8, 9, 0, 1
These input patterns should
never be encountered in practice
(hey -- it’s a BCD number!)
So, associated output values are
“Don’t Cares”

## Slide 17: K-map for BCD Increment Function
 |  | 00 | 01 | 11 | 10
00 |  | 1 |  |  | 1
01 |  | 1 |  |  | 1
11 |  | X | X | X | X
10 |  | 1 |  | X | X
A B C D
+ 1
W X Y Z
 |  | 00 | 01 | 11 | 10
00 |  |  |  |  | 
01 |  |  |  | 1 | 
11 |  | X | X | X | X
10 |  | 1 |  | X | X
 |  | 00 | 01 | 11 | 10
00 |  |  |  | 1 | 
01 |  | 1 | 1 |  | 1
11 |  | X | X | X | X
10 |  |  |  | X | X
 |  | 00 | 01 | 11 | 10
00 |  |  | 1 |  | 1
01 |  |  | 1 |  | 1
11 |  | X | X | X | X
10 |  |  |  | X | X
W
X
Z
Y
Z (without don’t cares) = A'D' + B'C'D’
Z (with don’t cares) = D'

## Slide 18: K-map Summary
Karnaugh maps as a formal systematic approach for logic simplification
2-, 3-, 4-variable K-maps
K-maps with “Don’t Care” outputs
H&H Section 2.7

## Slide 19: Sequential Logic Circuits and Design

## Slide 20: What We Will Learn Today
Circuits that can store information
  Cross-coupled inverter
  R-S Latch
  Gated D Latch
  D Flip-Flop
  Register
Finite State Machines (FSM)
  Moore Machine
  Mealy Machine
Verilog implementations of sequential circuits (next week)

## Slide 21: Circuits that Can Store Information

## Slide 22: Introduction
Combinational circuit output depends only on current input
We want circuits that produce output depending on current and past input values – circuits with memory
How can we design a circuit that stores information?
Sequential Circuit
Combinational
Circuit
inputs
outputs
Storage
Element

## Slide 23: Capturing Data

## Slide 24: Basic Element: Cross-Coupled Inverters
Has two stable states: Q=1 or Q=0.
Has a third possible “metastable” state with both outputs oscillating between 0 and 1 (we will see this later)
Not useful without a control mechanism for setting Q
Image source: Harris and Harris, Digital Design and Computer Architecture, 2nd Ed., p.110.

## Slide 25: More Realistic Storage Elements
Have a control mechanism for setting Q
  We will see the R-S latch soon
  Let’s look at an SRAM (static random access memory) cell first
We will get back to SRAM (and DRAM) later
SRAM cell

## Slide 26: The Big Picture: Storage Elements
Latches and Flip-Flops
  Very fast, parallel access
  Very expensive (one bit costs tens of transistors)
Static RAM (SRAM)
  Relatively fast, only one data word at a time
  Expensive (one bit costs 6+ transistors)
Dynamic RAM (DRAM)
  Slower, one data word at a time, reading destroys content (refresh), needs special process for manufacturing
  Cheap (one bit costs only one transistor plus one capacitor)
Other storage technology (flash memory, hard disk, tape)
  Much slower, access takes a long time, non-volatile
  Very cheap (no transistors directly involved)

## Slide 27: Basic Storage Element: The R-S Latch

## Slide 28: The R-S (Reset-Set) Latch
Cross-coupled NAND gates
  Data is stored at Q (inverse at Q’)
  S and R are control inputs
    In quiescent (idle) state, both S and R are held at 1
    S (set): drive S to 0 (keeping R at 1) to change Q to 1
    R (reset): drive R to 0 (keeping S at 1) to change Q to 0
S and R should never both be 0 at the same time
S
R
Q’
Q
Input |  | Output
R | S | Q
1 | 1 | Qprev
1 | 0 | 1
0 | 1 | 0
0 | 0 | Forbidden

## Slide 29: Why not R=S=0?
1
0
If R=S=0, Q and Q’ will both settle to 1, which breaks our invariant that Q = !Q’
If S and R transition back to 1 at the same time, Q and Q’ begin to oscillate between 1 and 0 because their final values depend on each other (metastability)
  This eventually settles depending on variation in the circuits (more metastability to come in Lecture 8)
S
R
Q’
Q
Input |  | Output
R | S | Q
1 | 1 | Qprev
1 | 0 | 1
0 | 1 | 0
0 | 0 | Forbidden
1
0
0
0
1
1

## Slide 30: The Gated D Latch

## Slide 31: The Gated D Latch
How do we guarantee correct operation of an R-S Latch?
S
R
Q’
Q

## Slide 32: The Gated D Latch
How do we guarantee correct operation of an R-S Latch?
  Add two more NAND gates!
  Q takes the value of D, when write enable (WE) is set to 1
  S and R can never be 0 at the same time!
S
R
Q’
Q
Write
Enable
D

## Slide 33: The Gated D Latch
S
R
Q’
Q
Write
Enable
D
Input |  | Output
WE | D | Q
0 | 0 | Qprev
0 | 1 | Qprev
1 | 0 | 0
1 | 1 | 1

## Slide 34: The Register

## Slide 35: The Register
D
Q
How can we use D latches to store more data?
Use more D latches!
A single WE signal for all latches for
simultaneous writes
D2
Q2
D1
Q1
D0
Q0
3
3
Write Enable
Here we have a register, or a structure that stores more than one bit and can be read from and written to
This register holds 4 bits, and its data is referenced as Q[3:0]

## Slide 36: The Register
How can we use D latches to store more data?
Use more D latches!
A single WE signal for all latches for
simultaneous writes
Register x (Rx)
D3:0
Q3:0
WE
4
4
Here we have a register, or a structure that stores more than one bit and can be read from and written to
This register holds 4 bits, and its data is referenced as Q[3:0]

## Slide 37: Memory

## Slide 38: Memory
Memory is comprised of locations that can be written to or read from. An example memory array with 4 locations:
Every unique location in memory is indexed with a unique address. 4 locations require 2 address bits (log[#locations]).
Addressability: the number of bits of information stored in each location. This example: addressability is 8 bits.
The entire set of unique locations in memory is referred to as the address space.
Typical memory is MUCH larger (billions of locations)
Addr(00):
Addr(10):
Addr(01):
Addr(11):
0100 1001
0010 0010
0100 1011
1100 1001

## Slide 39: Addressing Memory
Let’s implement a simple memory array with:
3-bit addressability & address space size of 2 (total of 6 bits)
D
Q
WE
1 Bit
Bit2
Bit1
Bit0
Bit2
Bit1
Bit0
Addr(0)
Addr(1)
6-Bit Memory Array
Notes: Memory array

## Slide 40: Reading from Memory
How can we select the address to read?
Because there are 2 addresses, address size is log(2)=1 bit
Notes: How do we read from memory?

## Slide 41: Reading from Memory
How can we select an address to read?
Because there are 2 addresses, address size is log(2)=1 bit
D[2]
D[1]
D[0]
Addr[0]
Wordline

## Slide 42: Reading from Memory
Address Decoder
How can we select an address to read?
Because there are 2 addresses, address size is log(2)=1 bit
D[2]
D[1]
D[0]
Addr[0]
Wordline

## Slide 43: Reading from Memory
Address Decoder
How can we select an address to read?
Because there are 2 addresses, address size is log(2)=1 bit
D[2]
D[1]
D[0]
Addr[0]
Multiplexer
Wordline

## Slide 44: Writing to Memory
How can we select an address and write to it?
Notes: How can we write to memory?

## Slide 45: Writing to Memory
How can we select an address and write to it?
Input is indicated with Di
Di[2]
Di[1]
Di[0]
Addr[0]
WE

## Slide 46: Putting it all Together
Di[2]
Di[1]
Di[0]
D[2]
D[1]
D[0]
Addr[0]
WE
Let’s enable reading and writing to a memory array
Notes: Putting it all together...

## Slide 47: A Bigger Memory Array
Di[2]
Di[1]
Di[0]
D[2]
D[1]
D[0]
Addr[1:0]
WE
Notes: A bigger memory array

## Slide 48: A Bigger Memory Array
Di[2]
Di[1]
Di[0]
D[2]
D[1]
D[0]
Addr[1:0]
WE
Address Decoder
Multiplexer

## Slide 49: Sequential Logic Circuits

## Slide 50: Sequential Logic Circuits
We have looked at designs of circuit elements that can store information
Now, we will use these elements to build circuits that remember past inputs
https://www.easykeys.com/228_ESP_Combination_Lock.aspx
https://www.fosmon.com/product/tsa-approved-lock-4-dial-combo
Sequential
Opens depending on past inputs
Combinational
Only depends on current inputs

## Slide 51: State
In order for this lock to work, it has to keep track (remember) of the past events!
If passcode is R13-L22-R3, sequence of states to unlock:
  The lock is not open (locked), and no relevant operations have been performed
  Locked but user has completed R13
  Locked but user has completed R13-L22
  Unlocked: user has completed R13-L22-R3
The state of a system is a snapshot of all relevant elements of the system at the moment of the snapshot
  To open the lock, states A-D must be completed in order
  If anything else happens (e.g., L5), lock returns to state A

## Slide 52: State Diagram of Our Sequential Lock
Completely describes the operation of the sequential lock
We will understand “state diagrams” fully later today
Image source: Patt and Patel, “Introduction to Computing Systems”, 2nd ed., page 76.

## Slide 53: Another Simple Example of State
A standard Swiss traffic light has 4 states
  Green
  Yellow
  Red
  Red and Yellow
The sequence of these states are always as follows
A
B
C
D

## Slide 54: Changing State: The Notion of Clock (I)
When should the light change from one state to another?
We need a clock to dictate when to change state
  Clock signal alternates between 0 & 1
At the start of a clock cycle ( ), system state changes
  During a clock cycle, the state stays constant
  In this traffic light example, we are assuming the traffic light stays in each state an equal amount of time
A
B
C
D
CLK:
0
1

## Slide 55: Changing State: The Notion of Clock (II)
Clock is a general mechanism that triggers transition from one state to another in a sequential circuit
Clock synchronizes state changes across many sequential circuit elements
Combinational logic evaluates for the length of the clock cycle
Clock cycle should be chosen to accommodate maximum combinational circuit delay
  More on this later, when we discuss timing

## Slide 56: Finite State Machines

## Slide 57: Finite State Machines
What is a Finite State Machine (FSM)?
  A discrete-time model of a stateful system
  Each state represents a snapshot of the system at a given time
An FSM pictorially shows
  1. the set of all possible states that a system can be in
  2. how the system transitions from one state to another
An FSM can model
  A traffic light, an elevator, fan speed, a microprocessor, etc.
An FSM enables us to pictorially think of a stateful system using simple diagrams

## Slide 58: Finite State Machines (FSMs) Consist of:
Five elements:
  A finite number of states
    State: snapshot of all relevant elements of the system at the time of the snapshot
  A finite number of external inputs
  A finite number of external outputs
  An explicit specification of all state transitions
    How to get from one state to another
  An explicit specification of what determines each external output value

## Slide 59: Finite State Machines (FSMs)
Each FSM consists of three separate parts:
  next state logic
  state register
  output logic
state register
At the beginning of the clock cycle, next state is latched into the state register

## Slide 60: Finite State Machines (FSMs) Consist of:
Sequential circuits
  State register(s)
    Store the current state and
    Load the next state at the clock edge
Combinational Circuits
  Next state logic
    Determines what the next state will be
  Output logic
    Generates the outputs
Notes: discuss DFlipFlop here. Latch doesn't do this, so we need sequential circuit that stores state and loads next state at the clock edge. next state is available for the full clock cycle
now lets take a look at this.

## Slide 61: Finite State Machines (FSMs) Consist of:
Sequential circuits
  State register(s)
    Store the current state and
    Load the next state at the clock edge
Combinational Circuits
  Next state logic
    Determines what the next state will be
  Output logic
    Generates the outputs
Notes: discuss DFlipFlop here. Latch doesn't do this, so we need sequential circuit that stores state and loads next state at the clock edge. next state is available for the full clock cycle
now lets take a look at this.

## Slide 62: State Register Implementation
How can we implement a state register? Two properties:
  1. We need to store data at the beginning of every clock cycle
  2. The data must be available during the entire clock cycle
CLK:
0
1
Register
Input:
Register
Output:
Desired behavior
Notes: Introduce clock much earlier maybe.
input data is sampled once.

## Slide 63: The Problem with Latches
Currently, we cannot simply wire a clock to WE of a latch
  Whenever the clock is high, the latch propagates D to Q
  The latch is transparent
D
Q
CLK = WE
CLK:
0
1
Register
Input:
Register
Output:
Recall the
Gated D Latch

## Slide 64: The Problem with Latches
Currently, we cannot simply wire a clock to WE of a latch
  Whenever the clock is high, the latch propagates D to Q
  The latch is transparent
D
Q
CLK = WE
CLK:
0
1
Register
Input:
Register
Output:
Recall the
Gated D Latch
Undesirable!

## Slide 65: The Problem with Latches
Currently, we cannot simply wire a clock to WE of a latch
  When the clock is high Q will not take on D’s value AND
  When the clock is low the latch will propagate D to Q
D
Q
CLK = WE
CLK:
0
1
Input:
Output:
Recall the
Gated D Latch
How can we change the latch, so that
1) D (input) is observable at Q (output)
only at the beginning of next clock cycle?
2) Q is available for the full clock cycle

## Slide 66: The Need for a New Storage Element
To design viable FSMs
We need storage elements that allow us
  to read the current state throughout the current clock cycle
  AND
  not write the next state values into the storage elements until the beginning of the next clock cycle.

## Slide 67: The D Flip-Flop
1) state change on clock edge, 2) data available for full cycle
D Latch (Slave)
D Latch (Master)
D
Q
CLK
When the clock is low, master propagates D to the input of slave (Q unchanged)
Only when the clock is high, slave latches D (Q stores D)
  At the rising edge of clock (clock going from 0->1), Q gets assigned D
CLK:
0
1

## Slide 68: The D Flip-Flop
1) state change on clock edge, 2) data available for full cycle
At the rising edge of clock (clock going from 0->1), Q gets assigned D
At all other times, Q is unchanged
CLK:
0
1
CLK
D
Q
Q
__
D Flip-Flop

## Slide 69: The D Flip-Flop
How do we implement this?
At the rising edge of clock (clock going from 0->1), Q gets assigned D
At all other times, Q is unchanged
CLK:
0
1
CLK
D
Q
Q
__
D Flip-Flop
We can use these Flip-Flops
to implement the state register!

## Slide 70: Rising-Clock-Edge Triggered Flip-Flop
Two inputs: CLK, D
Function
  The flip-flop “samples” D on the rising edge
  of CLK (positive edge)
  When CLK rises from 0 to 1, D passes
  through to Q
  Otherwise, Q holds its previous value
  Q changes only on the rising edge of CLK
A flip-flop is called an edge-triggered state element because it captures data on the clock edge
  A latch is a level-triggered state element
CLK

## Slide 71: Register
Multiple parallel flip-flops, each of which storing 1 bit
This register stores 4 bits
This line represents 4 wires
Condensed

## Slide 72: A 4-Bit D-Flip-Flop-Based Register (Internally)
Image source: Patt and Patel, “Introduction to Computing Systems”, 3rd ed., tentative page 95.

## Slide 73: Finite State Machines (FSMs)
Next state is determined by the current state and the inputs
Two types of finite state machines differ in the output logic:
  Moore FSM: outputs depend only on the current state

## Slide 74: Finite State Machines (FSMs)
Next state is determined by the current state and the inputs
Two types of finite state machines differ in the output logic:
  Moore FSM: outputs depend only on the current state
  Mealy FSM: outputs depend on the current state and the inputs

## Slide 75: Finite State Machine Example
“Smart” traffic light controller
  2 inputs:
    Traffic sensors: TA , TB (TRUE when there’s traffic)
  2 outputs:
    Lights: LA , LB (Red, Yellow, Green)
  State can change every 5 seconds
    Except if green and traffic, stay green
From H&H Section 3.4.1

## Slide 76: Finite State Machine Black Box
Inputs: CLK, Reset, TA , TB
Outputs: LA , LB

## Slide 77: Finite State Machine Transition Diagram
Moore FSM: outputs labeled in each state
  States: Circles
  Transitions: Arcs

## Slide 78: Finite State Machine Transition Diagram
Moore FSM: outputs labeled in each state
  States: Circles
  Transitions: Arcs

## Slide 79: Finite State Machine Transition Diagram
Moore FSM: outputs labeled in each state
  States: Circles
  Transitions: Arcs

## Slide 80: Finite State Machine Transition Diagram
Moore FSM: outputs labeled in each state
  States: Circles
  Transitions: Arcs

## Slide 81: Finite State Machine Transition Diagram
Moore FSM: outputs labeled in each state
  States: Circles
  Transitions: Arcs

## Slide 82: Finite State Machine: State Transition Table

## Slide 83: FSM State Transition Table
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | 
S0 | 1 | X | 
S1 | X | X | 
S2 | X | 0 | 
S2 | X | 1 | 
S3 | X | X | 

## Slide 84: FSM State Transition Table
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | S1
S0 | 1 | X | S0
S1 | X | X | S2
S2 | X | 0 | S3
S2 | X | 1 | S2
S3 | X | X | S0

## Slide 85: FSM State Transition Table
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | S1
S0 | 1 | X | S0
S1 | X | X | S2
S2 | X | 0 | S3
S2 | X | 1 | S2
S3 | X | X | S0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11

## Slide 86: FSM State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S’1 | S’0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11

## Slide 87: FSM State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S’1 | S’0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S’1 = ?

## Slide 88: FSM State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S’1 | S’0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S’1 = (S1 ∙ S0) + (S1 ∙ S0 ∙ TB) + (S1 ∙ S0 ∙ TB)

## Slide 89: FSM State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S’1 | S’0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S’1 = (S1 ∙ S0) + (S1 ∙ S0 ∙ TB) + (S1 ∙ S0 ∙ TB)
S’0 = ?

## Slide 90: FSM State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S’1 | S’0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S’1 = (S1 ∙ S0) + (S1 ∙ S0 ∙ TB) + (S1 ∙ S0 ∙ TB)
S’0 = (S1 ∙ S0 ∙ TA) + (S1 ∙ S0 ∙ TB)

## Slide 91: FSM State Transition Table
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S’1 | S’0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S’1 = S1 xor S0 (Simplified)
S’0 = (S1 ∙ S0 ∙ TA) + (S1 ∙ S0 ∙ TB)

## Slide 92: Finite State Machine: Output Table

## Slide 93: FSM Output Table
Current State |  | Outputs | 
S1 | S0 | LA | LB
0 | 0 | green | red
0 | 1 | yellow | red
1 | 0 | red | green
1 | 1 | red | yellow

## Slide 94: FSM Output Table
Current State |  | Outputs | 
S1 | S0 | LA | LB
0 | 0 | green | red
0 | 1 | yellow | red
1 | 0 | red | green
1 | 1 | red | yellow
Output | Encoding
green | 00
yellow | 01
red | 10
70

## Slide 95: FSM Output Table
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
LA1 = S1

## Slide 96: FSM Output Table
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
LA1 = S1
LA0 = S1 ∙ S0

## Slide 97: FSM Output Table
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
LA1 = S1
LA0 = S1 ∙ S0
LB1 = S1

## Slide 98: FSM Output Table
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
LA1 = S1
LA0 = S1 ∙ S0
LB1 = S1
LB0 = S1 ∙ S0

## Slide 99: Finite State Machine: Schematic

## Slide 100: FSM Schematic: State Register

## Slide 101: FSM Schematic: State Register

## Slide 102: FSM Schematic: Next State Logic
S’1 = S1 xor S0
S’0 = (S1 ∙ S0 ∙ TA) + (S1 ∙ S0 ∙ TB)

## Slide 103: FSM Schematic: Output Logic
LA1 = S1
LA0 = S1 ∙ S0
LB1 = S1
LB0 = S1 ∙ S0

## Slide 104: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 105: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 106: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 107: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 108: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 109: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 110: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 111: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB
This is from H&H Section 3.4.1

## Slide 112: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 113: FSM Timing Diagram
S0
LA: yellow
LB: red
S1
LA: yellow
LB: red
S2
LA: red
LB: green
S3
LA: red
LB: yellow
Reset
TA
TA
__
__
TB
TB

## Slide 114: Design of Digital Circuits Lecture 6: Sequential Logic Design
Prof. Onur Mutlu
ETH Zurich
Spring 2019
8 March 2019

## Slide 115: We did not cover the remaining slides. They are for your preparation for the next lecture.

## Slide 116: FSM State Encoding
How do we encode the state bits?
  Three common state binary encodings with different tradeoffs
    Fully Encoded
    1-Hot Encoded
    Output Encoded
Let’s see an example Swiss traffic light with 4 states
  Green, Yellow, Red, Yellow+Red

## Slide 117: FSM State Encoding
Fully Encoded:
  Minimizes # flip-flops, but not necessarily output logic or next state logic
  Use log2(num_states) bits to represent the states
  Example states: 00, 01, 10, 11
1-Hot Encoded:
  Maximizes # flip-flops, minimizes next state logic
  Simplest design process – very automatable
  Use num_states bits to represent the states
  Example states: 0001, 0010, 0100, 1000

## Slide 118: FSM State Encoding
Output Encoded:
  Minimizes output logic
  Only works for Moore Machines (output function of state)
  Each state has to be encoded uniquely, but the outputs must be directly accessible in the state encoding
  For example, since we have 3 outputs (light color), encode state with 3 bits, where each bit represents a color
  Example states: 001, 010, 100, 110
    Bit0 encodes green light output,
    Bit1 encodes yellow light output
    Bit2 encodes red light output

## Slide 119: FSM State Encoding
Output Encoded:
  Minimizes output logic
  Only works for Moore Machines (output function of state)
  Each state has to be encoded uniquely, but the outputs must be directly accessible in the state encoding
  For example, since we have 3 outputs (light color), encode state with 3 bits, where each bit represents a color
  Example states: 001, 010, 100, 110
    Bit0 encodes green light output,
    Bit1 encodes yellow light output
    Bit2 encodes red light output
The designer must carefully choose
an encoding scheme to optimize the design under given constraints

## Slide 120: Moore vs. Mealy Machines

## Slide 121: Moore vs. Mealy FSM Examples
Alyssa P. Hacker has a snail that crawls down a paper tape with 1’s and 0’s on it.
The snail smiles whenever the last four digits it has crawled over are 1101.
Design Moore and Mealy FSMs of the snail’s brain.

## Slide 122: Moore vs. Mealy FSM Examples
Alyssa P. Hacker has a snail that crawls down a paper tape with 1’s and 0’s on it.
The snail smiles whenever the last four digits it has crawled over are 1101.
Design Moore and Mealy FSMs of the snail’s brain.

## Slide 123: State Transition Diagrams
What are the tradeoffs?

## Slide 124: FSM Design Procedure
Determine all possible states of your machine
Develop a state transition diagram
  Generally this is done from a textual description
  You need to 1) determine the inputs and outputs for each state and 2) figure out how to get from one state to another
Approach
  Start by defining the reset state and what happens from it – this is typically an easy point to start from
  Then continue to add transitions and states
  Picking good state names is very important
  Building an FSM is like programming (but it is not programming!)
    An FSM has a sequential “control-flow” like a program with conditionals and goto’s
    The if-then-else construct is controlled by one or more inputs
    The outputs are controlled by the state or the inputs
  In hardware, we typically have many concurrent FSMs

## Slide 125: What is to Come: LC-3 Processor

## Slide 126: What is to Come: LC-3 Datapath

## Slide 127: Backup Slides: Different Types of Flip Flops

## Slide 128: The D Flip-Flop

## Slide 129: Enabled Flip-Flops
Inputs: CLK, D, EN
  The enable input (EN) controls when new data (D) is stored
Function:
  EN = 1: D passes through to Q on the clock edge
  EN = 0: the flip-flop retains its previous state

## Slide 130: Resettable Flip-Flop
Inputs: CLK, D, Reset
  The Reset is used to set the output to 0.
Function:
  Reset = 1: Q is forced to 0
  Reset = 0: the flip-flop behaves like an ordinary D flip-flop

## Slide 131: Resettable Flip-Flops
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop (see Exercise 3.10)
Synchronously resettable flip-flop?

## Slide 132: Settable Flip-Flop
Inputs: CLK, D, Set
Function:
  Set = 1: Q is set to 1
  Set = 0: the flip-flop behaves like an ordinary D flip-flop

## Slide 133: Recall: Combinational Logic Blocks

## Slide 134: Recall: Combinational Building Blocks
Combinational logic is often grouped into larger building blocks to build more complex systems
Hides the unnecessary gate-level details to emphasize the function of the building block
We now look at:
  Decoders
  Multiplexers
  Full adder
  PLA (Programmable Logic Array)

## Slide 135: Recall: Decoder
n inputs and 2n outputs
Exactly one of the outputs is 1 and all the rest are 0s
The one output that is logically 1 is the output corresponding to the input pattern that the logic circuit is expected to detect

## Slide 136: Recall: Multiplexer (MUX), or Selector
Selects one of the N inputs to connect it to the output
Needs log2N-bit control input
2:1 MUX

## Slide 137: Recall: Multiplexer (MUX)
The output C is always connected to either the input A or the input B
  Output value depends on the value of the select line S
Your task: Draw the schematic for an 8-input (8:1) MUX
  Gate level: as a combination of basic AND, OR, NOT gates
  Module level: As a combination of 2-input (2:1) MUXes